VELOCITY XL EMERGENCY FLIGHT OPERATIONS CHECKLIST N478B

| ▼OIL PRESSURE Oil Temp ( If normal, sensor misreading. Plan landing If high, land ASAP, plan power off landing ▲CYLINDER HEAD TEMPERATURE Mixture Richen Airspeed Increase IF NO CHANGE, PLAN POWER OFF LANDING ENGINE ROUGHNESS Mixture Adjust Magneto / EI ( IF NO CHANGE, PLAN POWER OFF LANDING ▲OIL TEMPERATURE Airspeed Increase Power Reduce IF NO CHANGE, PLAN POWER OFF LANDING ▲MECHANICAL NOISE Power Reduce IF NO CHANGE, PLAN POWER OFF LANDING ENGINE LOSS FLY THE AIRPLANE TO Roll In Flight Fuel Pump Off On Mixture Cut off Rich Throttle Closed Full Brakes Apply -- Master Sw. Off -- Starter Engage* * IF ENG. ROUGH, ( MIX AND IGN. LAND ASAP IF NO START, VG AND POWER OFF LANDING | ELECTRICAL FIRE FLY THE AIRPLANE Buses 1 and 2 Off Land ASAP ENGINE FIRE FLY THE AIRPLANE START GND FLIGHT Mixture Cut off Cut off Cut off Throttle Full Full -- Starter Switch On -- -- Ignition Switch -- Off Off Master Switch -- Off Off INFLIGHT DOOR OPENING FLY THE AIRPLANE Doors Close ASAP Fly Turns Away from open door Land ASAP LANDING WITH FLAT TIRE Land On good tire Near same side of runway Ailerons Keep weight off flat tire Landing Roll Lower nose gently ALTERNATOR FAILURE Electrical Load ▼to minimum safe flight Land As soon as practical POWER OFF LANDING FLY THE AIRPLANE Airspeed 90 (VG) Propeller Low RPM Radio/Xponder 121.5 / 7700 Disclose landing site ELT Activate Aim 1/3 of landing site Speed Brake Deploy if necessary Bus 1/2/Mag/EI Off Fuel Shut Valve Close (prior to touchdown) | ADVERSE OPERATIONS ENGINE HOT FLOOD Fuel Valve Open Mixture Rich (Cut off) Propeller Full Throttle Full (Full) Brakes On Buses 1 and 2 Bat Position Magneto / EI On Crossfeed Cold starts or ▼battery Strobes On Propeller Clear Start Safety Sw. On Starter Engage Mixture -- (Move fast rich) Throttle Retard (Move fast idle) Mixture Adjust. Lean ▲5K DA Oil Pressure 25 psi in 5 secs (or shut) Buses 1 and 2 Alternator position Voltage ( Annunciators Amps ( Positive charge EMS SHORT FIELD TAKEOFF Weight / CG Minimize / Close to aft limit Prop/Throttle Full from static position Brakes Minimum use for direction Elevator Full aft until rotation (65-75) Airspeed 80 kt (before obstacles) SOFT/ ROUGH FIELD TAKEOFF NOT RECOMMENDED Weight / CG Minimize / Close to aft limit Prop/Throttle ▲slowly. Start roll then full Brakes Minimum use for direction Elevator Full aft until rotation (65-75) Airspeed ▲in ground effect | SHORT FIELD LANDING Speed Brake Extend (below 110 kts) Trim Adjust Airspeed 75 kts (until flare) Throttle Idle (upon obstacles) Touchdown Main wheels Brakes Heavy SOFT/ ROUGH FIELD LANDING Airspeed 75 kts (until flare) Landing Roll Delay lowering the nose as long as possible BALKED LANDING (GO AROUND) Throttle Full Propeller 2700 RPM Mixture Rich Speed Brake Retract (if extended) Climb Speed - ▲90 SPEEDS Rotation Speed (VR) 65 -70 Best Angle Climb (VX) 80 Best Rate Climb (VY) 100 Maximum Structural (VNO) 170 Maneuvering (VA) 140 Never Exceed (VNE) 200 Speed Brake (VFE) 110 Glide (VG) 90 Landing Speed 75 Stall (Solo) (VS) 60 - 65 Maximum Crosswind Component Taxi 40 Take Off 15 Landing 20 |
| --- | --- | --- | --- |
| VELOCITY XL NORMAL FLIGHT OPERATIONS CHECKLIST N478B |
| CABIN PRE-FLIGHT GPS Flight Plan Set My Pilot Prayer Passenger Briefing Seatbelt/ Headset/ Conversation/ Traffic Distractions/ Turbulence/ Airsickness/ Doors Emergency Evacuations ENGINE Thro/Prop/Mix ¼” / Full / Full Brakes Test Buses 1 and 2 BAT position e-Checklists On Fuel Pump Five (5) seconds (> 5 psi) Crossfeed On cold starts/ ▼battery Magneto / EI On / On Start Safety Sw. On Strobes On Propeller Clear Starter Engage Buses 1 and 2 ALT position Oil Pressure ▲25 psi in 5 sec (or shut) Throttle/Mixture 1200 RPM - Lean – 800 Avionics On. (EFIS/EMS Left button) PCAS//GPS On Annunciators ( BEFORE TAXI Wind: 40 kts max. Fuel Quantity Add to EMS Nav-Comm ATIS/ AWOS. Note Set Gnd/Clearance/CTAF Altimeter Set Transponder Standby/ 1200 or Squawk Nav/Taxi Lights If required Ground/Traffic Contact | DURING TAXI Xwind Controls Dive to HW; turn from TW Elevator Trim Adjust to wt (▼0 – 1.5”) Flight Controls ( EFIS/EMS ( (Compass/Ball/Engine) Wind Sock ( RUN UP Magneto / EI ( 1800 RPM (▼175/50) Propeller Cycle ▼200-300 RPM max. ( ▼Oil Press / ▲MAP Amps/Volts >0A / >14v Charging Throttle Test idle ▼650; ▲800 Autopilot Test (overpower; turn off) Check Engine Parameters ( Oil Pressure 55 – 95 psi (Idle: 25) ( Oil Temp 100 - 200°F (245 max.) ( Fuel Pressure 18 – 40 psi (40 max.) ( CHT 200 - 400°F (500 max.) Seatbelts/Doors Secure (Visual/Lights) Nav-Comm Set Twr/ CTAF/ Clearance Tower/Traffic Request Clearance for TO Flasher Lights On PRE-TAKEOFF Speed Brake Up Fuel Pump On Mixture Rich (Lean to DA if rough) Annunciators ( / Pump On Xwind Comp If < 10 kts, ▲5 kts. If >10 kts, ▲½ gust factor Time Note Abort Plan Ready | TAKEOFF Xwind Comp Adjust Prop/Throttle ( Full Oil/Fuel Press ( 55-95 / 18 - 40 psi Rotate 70 (75-80 if DA ▲5K) CLIMB Airspeed 110-115 kts (80-120 kts). Fuel Pump Off ▲1500 ft AGL Prop 2700 (2500 Noise Abate) Mixture Rich (Lean to DA if rough) Oil Temp. ( 100 - 220°F (245° max.) CHT ( 200 - 400°F (435° max.) CRUISE Propeller 2200-2500 (▼75%) Trim Adjust Mixture ▼13 GPH (≤75%) then: Far: LOP ▼Rough ▲Smooth (50º last) Fast: ROP ▲from PK (50º first) (CHT CHT 200 - 400°F (500 max.) Engine Gauges ( Power Changes Use proper sequence Descent Rate Altitude to lose x3 = Miles Out DESCENT Elevator Lower nose Throttle/Prop Maintain settings Flasher Lights On Mixture Richen slowly, if rough PRE-LANDING (Pattern) Autopilot Off Throttle Adjust to 100 kts Fuel Pump On Prop/Mixture Full / Rich | LANDING (PATTERN) Xwind Comp If < 10 kts, ▲5 kts. If >10 kts, ▲½ gust factor Throttle / Trim (500 ft/min) Downwind 90 (95 kts GW) Base 85 (90 kts GW) Final 80 (85 kts GW) Speed brake when high or fast Landing Roll Lower nose gently Lower speed brake Use minimal brakes AFTER CLEARING RUNWAY Mixture Lean for taxi Fuel Pump Off Transponder Stand by Flashers Off SHUT DOWN Radios Off NORMAL Throttle ▲1200 RPM then idle EI/Mag Off / Off (Test Mag ground) QUICK STOPS Shut Off Valve Close Throttle Idle EI/Mag Off / Off Mixture Cutoff Start Safety Sw. Off HOBBS / Tach Note BUSES 1 AND 2 OFF Parking Brake Set as required Secure Aircraft Chocks / Tie Down / Pitot Control Surfaces Locks / Plugs / Doors |
| KIAS Stall: 60 -67 Best Angle Climb: 80 Best Rate Climb: 100 Maneuvering: 140 Max. Structural: 170 Max. Speed Brake: 110 Best Glide: 90 Never Exceed: 200 |