| VELOCITY XL PRE-FLIGHT INSPECTION CHECKLIST N478B |
| --- |
| COMPLETE FLIGHT PLAN PERFORM WEIGHT/BALANCE GENERAL INSPECTION Airplane Attitude and Shape ( Surface Condition ( Frost, Ice, Snow or Debris ( DETAILED INSPECTION COCKPIT (1) Aircraft Documents Airworthiness Cert./ Registration/ Limitations Charts/ Aircraft Manual/ Pilot Documents Fire Extinguisher ( Overhead Switches Off Fuel Sight Gauges ( Record fuel Throttle Idle Propeller Full Mixture Cutoff Propeller Area Clear Bus #1 Switch On | Speed Brake Down Lights ( (as needed) Pitot Tube Heat ( Bus #1 Switch Off Alternate Cabin Air Closed Nose Access Cover Open Fuel Sampler / Flashlight FUSELAGE/ LEFT LEADING EDGE (2) Static Port Clear Door Hinges/ Latches ( Fuel Cap Secure Strake Surface ( Vortilons ( Wing Surface ( Landing Light ( LEFT WING TIP (3) Nav Light/ Strobe ( Winglet Condition ( Rudder Clip Remove Rudder ( LEFT WING TRAILING EDGE (4) Wing Surface ( Trailing Edge ( Aileron Clip Remove Aileron ( Tie-Down ( Strake Surface ( Fuel Leaks ( Main Gear Tire ( Wear / 55 psi / Chocks Brakes ( Calipers, Pads, Leaks Wheel Pant ( | ENGINE/ PROPELLER (5) Transponder Antenna ( Fuel Vents REMOVE FLAG Fuel Contaminants ( First flight / After refueling Cowling Exterior ( Surface, Screws Exhaust Stacks ( Tightness, Integrity Cowling Interior ( Pins, Oil Leaks, Electrical, Starter, Flywheel, Plenum Magneto Coupling ( Propeller / Spinner ( Nicks/ cracks, screws, safety wire, leaks Engine Oil ( 7 qts (8 long trips) Oil Filler Cap / Accessory Door Secure RIGHT WING TRAILING EDGE (6) Strake Surface ( Fuel Leaks ( Main Gear Tire ( Wear / 55 psi / Chocks Brakes ( Calipers, Pads, Leaks Wheel Pant ( Tie-Down ( Wing Surface ( Trailing Edge ( Aileron Clip Remove Aileron ( RIGHT WING TIP (7) Rudder Clip Remove Rudder ( Winglet Condition ( Nav Light/ Strobe ( | FUSELAGE/ RIGHT LEADING EDGE (8) Landing Light ( Vortilons Secure Wing Surface ( Fuel Cap Secure Strake Surface ( Static Port Clear Door Hinges/ Latches ( CANARD RIGHT (9) Sparrow Strainer ( Attachment, Integrity Canard/Elevator Surface ( Elevator Hinges / Movement ( Canard Attachment ( Counterweight ( NOSE (10) Pitot Tube REMOVE FLAG Canard Cover Attachment ( Nose Compartment ( Taxi Light, Batteries, Electrical, Brake Fluid, Oil Leaks, Oil Cooler, Canard Cover Pins Store: Fuel Sampler, Clips, Chocks, Flashlight BALLAST Per W&B Nose Access Cover ( Latch / Secure Nose Wheel ( Tire, Pressure (45 psi) ( Damper, Fork, Wheel Pant CANARD LEFT (11) Canard/Elevator Surface ( Counterweights ( Elevator Hinges ( Static Port Clear |

| VELOCITY XL PRE-FLIGHT INSPECTION CHECKLIST N478B |
| --- |
| COMPLETE FLIGHT PLAN PERFORM WEIGHT/BALANCE GENERAL INSPECTION Airplane Attitude and Shape ( Surface Condition ( Frost, Ice, Snow or Debris ( DETAILED INSPECTION COCKPIT (1) Aircraft Documents Airworthiness Cert./ Registration/ Limitations Charts/ Aircraft Manual/ Pilot Documents Fire Extinguisher ( Overhead Switches Off Fuel Sight Gauges ( Record fuel Throttle Idle Propeller Full Mixture Cutoff Propeller Area Clear Bus #1 Switch On | Speed Brake Down Lights ( (as needed) Pitot Tube Heat ( Bus #1 Switch Off Alternate Cabin Air Closed Nose Access Cover Open Fuel Sampler / Flashlight FUSELAGE/ LEFT LEADING EDGE (2) Static Port Clear Door Hinges/ Latches ( Fuel Cap Secure Strake Surface ( Vortilons ( Wing Surface ( Landing Light ( LEFT WING TIP (3) Nav Light/ Strobe ( Winglet Condition ( Rudder Clip Remove Rudder ( LEFT WING TRAILING EDGE (4) Wing Surface ( Trailing Edge ( Aileron Clip Remove Aileron ( Tie-Down ( Strake Surface ( Fuel Leaks ( Main Gear Tire ( Wear / 55 psi / Chocks Brakes ( Calipers, Pads, Leaks Wheel Pant ( | ENGINE/ PROPELLER (5) Transponder Antenna ( Fuel Vents REMOVE FLAG Fuel Contaminants ( First flight / After refueling Cowling Exterior ( Surface, Screws Exhaust Stacks ( Tightness, Integrity Cowling Interior ( Pins, Oil Leaks, Electrical, Starter, Flywheel, Plenum Magneto Coupling ( Propeller / Spinner ( Nicks/ cracks, screws, safety wire, leaks Engine Oil ( 8 qts (▲long trips) Oil Filler Cap / Accessory Door Secure RIGHT WING TRAILING EDGE (6) Strake Surface ( Fuel Leaks ( Main Gear Tire ( Wear / 55 psi / Chocks Brakes ( Calipers, Pads, Leaks Wheel Pant ( Tie-Down ( Wing Surface ( Trailing Edge ( Aileron Clip Remove Aileron ( RIGHT WING TIP (7) Rudder Clip Remove Rudder ( Winglet Condition ( Nav Light/ Strobe ( | FUSELAGE/ RIGHT LEADING EDGE (8) Landing Light ( Vortilons Secure Wing Surface ( Fuel Cap Secure Strake Surface ( Static Port Clear Door Hinges/ Latches ( CANARD RIGHT (9) Sparrow Strainer ( Attachment, Integrity Canard/Elevator Surface ( Elevator Hinges / Movement ( Canard Attachment ( Counterweight ( NOSE (10) Pitot Tube REMOVE FLAG Canard Cover Attachment ( Nose Compartment ( Taxi Light, Batteries, Electrical, Brake Fluid, Oil Leaks, Oil Cooler, Canard Cover Pins Store: Fuel Sampler, Clips, Chocks, Flashlight BALLAST Per W&B Nose Access Cover ( Latch / Secure Nose Wheel ( Tire, Pressure (45 psi) ( Damper, Fork, Wheel Pant CANARD LEFT (11) Canard/Elevator Surface ( Counterweight ( Elevator Hinges ( Static Port Clear |