| VARIOUS FLYING REFERENCES |
| --- |
| XWIND COMP | 0 to 30º = .5 x Wind Speed 30 to 45º = .75 x Wind Speed > 45º = Wind Speed |
| DENSITY ALTITUDE | STANDARD OAT: ▼ 3.5ºF per 1,000’ altitude. DA: ▲ 60’ per degree above std OAT. EXAMPLE: AIRPORT ELEVATION: 6,000’ OAT: 80ºF Determine std OAT for elevation: Elev. in 1,000 (6) x -3.5 + 60 = 39 Subtract from actual OAT: 80 - 39 = 41 Multiply by 60’: 41 x 60 = 2,460 Add to field elevation: 2,460 + 6,000 = 8,460 |
| TAKEOFF | POWER AVAILABLE: Multiply altitude (in 1,000’) by 3 and subtract from 100% TAKEOFF ROLL: Add 10% distance per every 1,000 DA increase up to 8K, and 15% if >8K. ABORT: If 75% of VR (45 knots) is not achieved by mid-runway. OBSTACLES: Increase in DA reduces climb angle and ability to clear obstacles on takeoff. |
| WEIGHTS SPEEDS | Speeds are affected in half (%) of what the aircraft weight (%) is changed. If aircraft weight ▲by 20%: Maneuvering Speed will ▼ by 10% and vice versa Stall Speed will ▲ by 10% |
| FUEL CONSUMPTION | Multiply necessary hours of flight by 15 for fuel requirement. Divide gallons of fuel remaining in tanks by 15 for remaining flight time. |
| ALTITUDE | Subtract MAP reading (at full throttle) from 30 and multiply by 1,000’ |
| KIAS to KTAS | Multiply altitude (in 1000’s of feet) by 5 and add to KIAS |
| ENROUTE WEATHER | Contact Flight Watch on 122.0 (at 5,000’ AGL or higher) “( ) Flight Watch, Experimental Velocity 478B, 20 north of the ( ) VOR, over.” |
| PIREPs | Flight Watch (122.0 ▲5K’) / 1-800-WX-BRIEF (after landing.) NO MINIMUM ITEMS ARE REQUIRED. TYPE OF REPORT: (Routine (Urgent NEAREST VOR/AIRPORT: _______________________________________ OBSERVATION TIME: _____ minutes ago ALTITUDE: _______SL AIRCRAFT TYPE: Exp. Velocity N478B (VELO) CLOUD COVERAGE: (CLR (FEW (SCT (BKN (OVC CLOUD TYPE: (Cirrus (Cumulus (Stratus CLOUD HEIGHT: Bases:___________ Tops:___________ VISIBILITY: ____ Statute Miles VISIBILITY RESTRICTIONS: (Haze (Mist (Fog (Dust (Sand Other:______ PRECIPITATION TYPE: (Rain (Drizzle (Snow (Hail PRECIPITATION INTENSITY: (Light (Moderate (Heavy TEMPERATURE: _____Celsius WIND DIRECTION: ____ _º Speed: _____Knots TURBULENCE: (Light (L. Chop ( Moderate (Mod. Chop (Severe (Extreme ICING: (Trace (Light (Moderate (Severe REMARKS: |
| DESCENT | GPS Descend at 500 ft/min: When descending altitude is half the time to the airport. When time to airport is double the descending altitude. Descend at 750 ft/min: When descending altitude is one third the time to the airport. When time to airport is triple the descending altitude. CALCULATE DESCENDING DISTANCE (DD) Calculate Descending Altitude: Altitude – Field Elevation (Feet) Calculate Distance: (KTAS ÷ 60) x Descending Altitude 120 KTAS (2.00 NM/Min) 140 KTAS (2.33) 160 KTAS (2.66) 180 KTAS (3.00) CALCULATE RATE OF DESCENT Determine DISTANCE TO DESTINATION (DtD) in NM. (26) NM Calculate TIME TO DESTINATION: KTAS ÷ Speed Factor) (11 .15) Minutes Divide Descending Altitude by Time to Destination (670) Feet/min |
| LANDING | If unable to touch down on first third of runway, go around. |
| FAA FLIGHT PLAN |
| 1. Type: VFR / IFR / DVFR | 9. Destination Point: |
| 2. Aircraft ID: N478B | 10. Estimated Time Enroute: 00:00 |
| 3. Aircraft Type / Equipment: VELO / U | 11. Remarks |
| 4. True Airspeed: 165 KTAS | 12. Fuel on Board: 00:00 |
| 5. Departure Point: | 13. Alternate Airports |
| Departure Time (Z) Proposed: Actual: | 14: Pilot Address / Telephone Aircraft Home Base: WJF |
| 7. Cruising Altitude: | 15. Number on Board: |
| 8. Route of Flight: | 16. Color of Aircraft: White with Brown/Copper design |

| ENGINE LEANING GUIDE |
| --- |
| ENGINE START | NORMAL Mixture: Rich Throttle: 1200 RPM Mixture: Lean until rough; then richen until smooth. Throttle: 800 - 1000 RPM |
| TAXI – RUN UP | Propeller. Cycle |
| TAKE OFF | Mixture / Propeller / Throttle Full |
| CLIMB | Propeller: 2500 – 2700 RPM Mixture: Full rich. Lean if rough. |
| CRUISE | FAST Mixture: Lean fast (2-3 seconds) to 13 GPH. Richen to maintain CHT (380º - 390º F). FAR (62%) Mixture: Lean fast (2-3 seconds) to 13 GPH. Lean further until rough. Richen until smooth. Maintain CHT (380 - 390º F). |
| DESCENT | Lower nose Mixture: Richen progressively if rough or low CHTs |
| LANDING | Throttle: Reduce Propeller: Full Mixture: Rich (Optional) |
| SHUTDOWN | Throttle: 1200 RPM for 10 seconds: then to idle Turn off the EI Turn off the magneto The engine should shut down. If not, the magneto is hot (not grounded) and engine may start with propeller rotation. |

# Text boxes

Draw a line between the airport’s temperature and pressure altitude. Multiply the factors crossed by the airplane’s sea level take off distance and climb rate to obtain expected density altitude performance.

Take Off Distance:  1,500 ft

Climb Rate:  750 ft/min